## Slide 1: Quantum Computers: Fundamentals, Applications and Implementation
Ben Feldman, Harvard University
Big Techday Conference
June 14, 2013
Image: Introduction to quantum information processing review, Science 339, 1163 (2013).
z = |0 >
-z = |1 >
x
y
θ
φ
|ψ >
ˆ
ˆ
ˆ
ˆ

## Slide 2: Motivation: Future of Computers
Moore’s law
Moore, G. E. Electronics 8, 114–117 (1965).
Image from: Ferain, I. et al., Nature 479, 310–316 (2011).
…will soon run into major physical constraints
Silicon
Source
Drain
Gate
Insulator
2020
1 nm
0.1 nm
(atomic radius)
2030
2040
2050
?

## Slide 3: Limitations of Classical Computers
RSA encryption (2048-bit)
  100,000 computers in parallel
  3 GHz processors
  Factoring would take longer than the age of the universe
Quantum Simulation: inefficient with classical computers
  Feynman: why not use quantum mechanics for computation?

## Slide 4: Outline
What are quantum computers?
  Classical vs. quantum bits
Problems suited to quantum computation
How to realize a quantum computer

## Slide 5: Outline
What are quantum computers?
  Classical vs. quantum bits
Problems suited to quantum computation
How to realize a quantum computer

## Slide 6: Standard Computers
Classical bits + Logic and Memory = Computer
  0
  + =
  1

## Slide 7: Quantum Bits (qubits)
Classical Bits
Can be only 0 or 1
OR
Qubits
Superposition of both 0 and 1
AND
Any quantum two-level system can act as a qubit, e.g.
  Atoms
  Spins
Notes: 300 qubits = 1 bit per atom in the universe

## Slide 8: Quantum Bits (Qubits)
z = |0 >
-z = |1 >
x
y
θ
φ
|ψ >
ˆ
ˆ
ˆ
ˆ
Quantum Bit:
|ψ > = cos(θ/2)|0> + eiφsin(θ/2)|1>
= a|0> + b|1>
Any vector pointing to the surface of the sphere is a valid quantum state!

## Slide 9: Quantum Bits (qubits)
Classical Bits
Can be only 0 or 1
OR
Need 2N classical bits to encode the same amount of information as N qubits
Qubits
Superposition of both 0 and 1
AND
1 qubit: a|0> + b|1>
2 qubits: a|00> + b|01> + c|10> + d|11>
3 qubits: a|000> + b|001> + c|010> + d|100> + e|011> + f|101> +g|110> + h|111>
Notes: 300 qubits = 1 bit per atom in the universe

## Slide 10: But…Measurement Limits You
a|0> + b|1>
|0>
|1>
Measurement
After measurement, quantum state collapses, information is lost!
Image adapted from: http://en.wikipedia.org/wiki/Stern-Gerlach_experiment
Notes: 300 qubits = 1 bit per atom in the universe

## Slide 11: Paradox: Schrödinger’s Cat
Cat would be in a ‘superposition’ of alive and dead at the same time!
Schrödinger’s Cat
Image from: http://en.wikipedia.org/wiki/Schrödinger’s_cat

## Slide 12: How Can You Benefit?
If measurement changes the answer, how can you fully utilize the 2N states?
The key: use ‘hidden’ information with a clever algorithm
Still, in some cases, qubits still pay off!

## Slide 13: Example: f(x)={0,1} for x = 0 or 1
Consider f(x)
  Input: either 0 or 1
  Output: either 0 or 1
Classically, you need at least two evaluations to determine if f(0) = f(1)
Using quantum gates, you need only one!

## Slide 14: Deutsch Algorithm
Measure
Start with states along +x and -x:
    [|0> + |1>][|0> - |1>]
Perform y xor f(x)
    [|0> + |1>] [(|0> xor |f(x)>) - (|1> xor |f(x)>)]
    (-1)f(x)[|0> + |1>][|0> - |1>]
      For f(0) = f(1): ±[|0> + |1>][|0> - |1>]
      For f(0) ≠ f(1): ±[|0> - |1>][|0> - |1>]
z = |0 >
-z = |1 >
x
y
ˆ
ˆ
ˆ
ˆ = |0> + |1>
[|0> - |1>]
[|0> + |1>]
f(0)=f(1): ±[|0> + |1>]
f(0)≠f(1): ±[|0> - |1>]
x x
y y xor f(x)
[|0> - |1>]
XOR | 0 | 1
0 | 0 | 1
1 | 1 | 0

## Slide 15: So What Have We Learned?
We determined a global property of the system faster than is possible classically
  We can learn if f(0)=f(1) with one function evaluation
  We can’t learn their value though! (One calculation gives only one bit of information)
Only a multiplicative factor speedup, but example is illustrative

## Slide 16: Outline
What are quantum computers?
  Classical vs. quantum bits
Problems suited to quantum computation
How to realize a quantum computer

## Slide 17: RSA encryption
  Recall: 100,000 computers in parallel operating at 3 GHz, RSA factoring would take longer than the age of the universe
  Quantum computation allows a speedup from exponential to polynomial time!
    A single 1 MHz quantum computer could do it in about 1 minute
Shor’s Algorithm
L. M. K. Vandersypen et al., Nature 414, 883 (2001).

## Slide 18: Factorization Accomplishments
2001: 15=5x3
2012:
  21=7x3 (iterative method)
  143=13x11 (adiabatic quantum computer)
But don’t worry, quantum mechanics can be used for secure encryption as well!
L. M. K. Vandersypen et al., Nature 414, 883 (2001).
E. Martin-Lopez et al., Nat. Photonics. 6, 773 (2012).
N. Xu et al., Phys. Rev. Lett. 108, 130501 (2012).

## Slide 19: Classical search
Searching an unsorted list classically: no better way than guess and check (order N)

## Slide 20: Quantum search: Grover’s Algorithm

## Slide 21: Quantum search: Grover’s Algorithm

## Slide 22: Quantum search: Grover’s Algorithm
Quantum search:
order N1/2

## Slide 23: Other Potential Applications
Traveling salesman problem
Quantum Simulation
Protein conformation, or other problems with many variables (weather, stock market)
Images from:
http://www.ornl.gov/info/ornlreview/v37_2_04/article08.shtml
L. Fallani, M. Inguscio, Science, 322, 1480 (2008).
http://en.wikipedia.org/wiki/Protein_structure

## Slide 24: Outline
What are quantum computers?
  Classical vs. quantum bits
Problems suited to quantum computation
How to realize a quantum computer

## Slide 25: Steps to Build a Quantum Computer
Roadmap toward realizing a quantum computer
M. H. Devoret and R. J. Schoelkopf, Science, 339, 1169 (2013).

## Slide 26: Classical Error Correction
Simply make three identical bits, and use majority rules
Majority vote wins
Perform
Operation

## Slide 27: What about errors?
No-cloning theorem: in general, it’s impossible to copy a qubit
Measurement collapses a quantum state
  How do you even tell if an error has occurred?
“Analog”-like system: continuous errors are possible
a|0> + b|1>
a|0> + b|1>
a|0> + b|1>

## Slide 28: Quantum Error Correction is Possible
Errors can be found without performing a quantum measurement
Error rate threshold for fault-tolerant quantum computation: <10-4 to 10-6
Many ancillary qubits likely necessary for each logical qubit, but it can be done!

## Slide 29: Qubit Control vs. Isolation
Fundamental dichotomy:
  Any interaction with environment is bad: it ‘decoheres’ qubits (acts as a measurement)
  Yet we want full control over the qubit

## Slide 30: Proposed QC Schemes
Strong control over qubits
  Trapped ions/atoms
  Superconducting circuits
  Spins in various materials
Isolation from decoherence
  Topologically protected states
Quantum annealing (its own separate topic)

## Slide 31: Ion Traps
Electrostatic traps hold ions in place (in vacuum)
  Motion of ions serves to couple qubits
Technology developed first, and still “furthest along”: 14 qubits (2011)
T. Monz et al., Phys. Rev. Lett. 106, 130506 (2011).; L. Fallani, M. Inguscio, Science, 322, 1480 (2008).

## Slide 32: Superconducting and Spin Qubits
Superconducting qubits: aluminum circuits
  Amount of charge, Direction of superconducting current, Phase of current across a junction
Spins
  Defect centers in diamond, silicon
  Artificial atoms
Image courtesy of M.D. Shulman
http://web.physics.ucsb.edu/~martinisgroup/

## Slide 33: Topologically Quantum Computation
First move in X, then in Y:
First move in Y, then in X
Front
Top
Side
Front
Top
Side
vs.
For most things: order of operations doesn’t matter
You get the same result either way

## Slide 34: Topologically Protected States
“Non-abelian” states: order of operations matters
Insensitive to noise from environment
First rotate around X, then around Y: different result!
First rotate around Y, then around X
Front
Top
Side
Top
Side
Side
Top
x
y

## Slide 35: Summary of Qubit Approaches
Qubit type | Advantages | Weaknesses
Ion/atom Trap | -Extremely good quantum state control -Little interaction with environment -All ions are identical | -Difficult to scale up the number of qubits
Superconducting | -Compatible with current lithography procedures -Electrical control | -Each qubit is slightly different due to fabrication imperfections
Spins | Depending on the system: -Potentially long coherence times -Optical and/or electrical control possible -Room temperature operation | -Each qubit may be slightly different -Difficult to isolate from the environment
Topological | -Insensitivity to noise in the environment | -Forming topologically protected states is difficult -No demonstrated qubits yet

## Slide 36: Putting it all Together
Likely final solution: combined technology that takes advantage of the strengths of each approach
D.D. Awschalom et al., Science, 339, 1174 (2013).
For example:
-Trapped ions for long-lived qubit states
-Spin qubits for readout
-Superconducting circuitry for quantum buses

## Slide 37: Quantum Annealing
Many problems can be mapped onto the question: What is the ground state?
  Initialize a known problem in its ground state.
  Transform into a problem of interest. Go slowly so that you stay in the ground state.
  Nature has solved the problem for you!
M. W. Johnson et al., Nature 473, 149 (2011).

## Slide 38: Quantum Annealing: D-wave
D-wave makes and sells quantum annealers (superconducting qubit base)
Lockheed Martin: bought a 128-qubit model
Google and NASA: bought one with 512 qubits to work on artificial intelligence
But: debate in community whether these are true quantum computers, and if they’re better than classical algorithms
See: http://www.dwavesys.com/en/dw_homepage.html http://scottaaronson.com/blog

## Slide 39: Conclusions and Outlook
Quantum computing is very much in its infancy
Already, several ideas for applications
Nobody can predict what might come out; who could have imagined the internet in 1950?